## Slide 1: Team 10: Malawi Washing Machine
Team: Wesley Eidt, Jake Erwin, Bradley Franks, Ryan Kinkade, and Kyle Wilson
Advisors: Dr. Scott Thomas and Dr. Thomas Hangartner
Notes: Ryan

## Slide 2: Malawi
One of the world’s poorest countries
Landlocked
No electricity
No running water
Illiteracy
  Oral Tradition
Notes: Ryan

## Slide 3: Design Constraints
Build a human-powered washing machine.
Needs to use materials readily available in Malawi.
Easy to build and communicate.
Notes: Ryan

## Slide 4: Previous Designs
Two previous designs
2017 design:
  Bike power
  Tilted barrel
  Rotating agitator
2018 design:
  Complex frame
  Distributed torques
  Rotating agitator
Design from 2017 Team
Design from 2018 Team
Notes: Ryan

## Slide 5: Agitation
Similar to previous design.
Central shaft
  Fins radiate
Different fin orientations
Different fin numbers
  Single, double, and triple
Each tested for agitation quality and difficulty of use.
Notes: Bradley

## Slide 6: Agitation
Mono-fin, Bi-fin, and Tri-fin
Bi-fin showed best performance
  Easiest assembly for highest effectiveness
Agitator Comparisons |  |  | 
Fin | Mono-Fin | Bi-Fin | Tri-Fin
Agitation | 3 | 8 | 10
Ease of Construction | 10 | 9 | 3
Weight | 10 | 9 | 4
Communicability | 10 | 8 | 2
Total | 33 | 34 | 19
Notes: Bradley

## Slide 7: Frame
Test frame
  Made from wooden planks.
  Simple to build and adjust.
  Served as a convenient placeholder.
Final metal frame
  Welded from ½" steel tubing.
  Allows for variable tube lengths / dimensions.
  Sized to hold either plastic or metal barrel.
Notes: Wes

## Slide 8: Bearings
Support central shaft
  Allow for low friction rotation.
  Prevent metal on PVC contact.
  Attach to metal frame and prevent excess shaft movement.
Boiling PVC
  Made from a larger-diameter PVC pipe than the shaft.
  Shape large pipe around the smaller during construction.
Notes: Wes

## Slide 9: Stepper
Lever pushed by operator
  Impacts ratchet to spin shaft and agitator.
Requires separate frame to hold lever.
  Rotates on PVC axle.
Fixed to frame to maintain alignment.
Notes: Jake

## Slide 10: Ratchet and Pawl
Transmission
  Translates user's input to spinning of agitator.
  Locks rotation to one direction.
  Driving pawl and locking pawl
Manufacturability
  Must be created from materials available.
  Teeth must be straight.
Notes: Jake

## Slide 11: Molds
In order to create a concrete gear, we needed a precise mold.
Molds were developed to make a ratchet.
Attempted molds with Bondo, cornstarch, soap, and silicone.
Never able to achieve an ideal formula.
  Some molds did not set.
  Others did not show definition.
Notes: Wes

## Slide 12: Ratchet
After trouble with molding, an alternative was developed.
Updated design created using threaded rods.
  Rods serve as teeth.
New problems
  Difficulty with nut security
  Difficulty with rod alignment
Stepper-ratchet system had flaws.
  Difficulty delivering force
  Poor retention of momentum
Notes: Jake

## Slide 13: Hand Crank
Hand Crank designed to apply direct power.
Variety of designs.
Low required input torque (approximately 4 to 9 ft-lbs)
Notes: Jake

## Slide 14: Assembly
Hand-crank agitator effectively washes clothes.
Handles can be simply constructed and substituted for user preference.
"Simpler is better."
  Easy to obtain parts, construct, and communicate.
Notes: Kyle

## Slide 15: Budget
Total Funds | $1,000.00
Total Expenses | $554.78
Remaining Funds | $445.22
Expenses by Category | Cost
Agitator | $135.89
Mold Testing | $108.18
Frame | $130.28
Equipment and Misc. | $70.43
Total cost of barrel design:
  $231.10
Cost of manufacturing frame:
  $72.00
Notes: Kyle

## Slide 16: Acknowledgements
A special thanks to Dr. Lynn Rogers and Dr. Bill Wollenhaupt for the donation of a plastic barrel and a great amount of advice. Thanks to the Hangartner’s for their advice and information that they provided. Thanks to Mike Erwin for the use of his welding equipment. Thanks to Kevin Eidt for creating custom metal pieces for the project. And a thank you to Marcus Acton for the donation of a metal barrel. Without the help of these individuals, it would have been very difficult to complete this project.
Notes: Kyle

## Slide 17: Questions?
Notes: Kyle

## Slide 18: References
http://www.technologystudent.com/cams/ratch1.htm
http://www.notesandsketches.co.uk/Ratchet.html
https://upload.wikimedia.org/wikipedia/commons/4/46/Malawi_map.png
http://www.technologystudent.com/cams/ratch1.htm
Grey, R., Hatton, N., Kosey, K., Lippolis, R. and Salchak, S. (2017). Washing Machine. [image].
Moussa, H., Purvis, J. and Spencer, Z. (2018). Washing Machine. [image].